## Slide 1: Orion Project
Carbon mast

## Slide 2: Introduction
In view of the lack of available masts as well as the costs of producing a relatively small amount of Aluminum masts ISA executive has decided to support a trial / pilot with carbon fiber masts under strict rules and regulations from the International Soling Class.
Carbon masts have been used for Olympic class yachts and beyond for over 20 years now.
All classes using carbon masts have proven that they can last longer and are a lot harder to break.
ISA Letter

## Slide 4: Measurements

## Slide 5: INTERNATIONAL SOLING CLASS RULES
Section F — Rig
F.1 Certification
F.1.1 The rig shall comply with the class rules in force at the time of initial
fundamental measurement.
F.1.2 Measurement shall carried out in accordance with the ERS.
F.1.3 Routine maintenance is permitted, but altered or repaired spars shall be remeasured.
F.2 Mast
F.2.1 MANUFACTURER
Manufacturer is optional.
F.2.2 MATERIALS
F.2.2.1 The mast spar shall be one continuous drawn aluminium alloy extrusion with
an integrated groove. The aluminium content shall be minimum 90%.
F.2.2.2 Holes may be made in the mast only for fittings and rigging
Carbon
see data sheet
F.2.4.10 Mast weight The sectional weight including the luff groove shall be not less than 2.20kg/m.
Checken
New rule
The centre of gravity must be above the spreaders

## Slide 6: INTERNATIONAL SOLING CLASS RULES
F.2.4.11 Tip weight ................................................................…11 kg
(a) The mast complete with all standing and running rigging and supported
at the band defined in Rule F.2.4.5 (a) shall weigh not less than 11kg
when it is weighed at the band defined in Rule F.2.4.5 (c).
(b) For the purpose of this measurement the halyards shall be fully hoisted
and the standing rigging secured along the mast. The ends of the
rigging below the band defined in rule F.2.4.5 (a) may rest on the
ground or be removed so as not to affect the tip weight. The weight of
the spinnaker shackle, for the purpose of tip weight, shall not be more
than 70gr.
(c) The mast shall not be disqualified if a shortfall in the weight measured in
accordance with Rule F.2.4.10 can be corrected by the fixing of a
corrector weight of not more than 300gr at a point above the top band.
The corrector weight shall be fixed by a screw fitting (bolt and nut)
attached through holes drilled in the mast or crane.
(d) For the purposes of Rule F.2.4.10 any readily removable fittings such as
a wind indicator shall be removed.
2,7 kg
500 mm at the top

## Slide 7: Design Questions and answers
Why didn’t we add extra material to balance the top weight?
  If we add material the charactiristics would be very different. This mast has the same bending performance as the aluminium mast.
Main(only) reason to develop the carbon mast.
  No good aluminium masts available on the market.
  Low cost for small quantities
Durability.
  Carbon will last longer.